原級速率接取界面測試項目表

(E1介面【2.048Mbit/s】)

1.Layer 1 Conformance Test

Test Suite: CHT-98-PA-L1               Verdicts Assigned

PASS:       5

FAIL:       0

INCONC:     0

Selected Cases:    5

Test Identifier     				ITU-T REC. I.431		Verdict

Test Group: Electrical/Functional

characteristic test

1. Bit rate   						4.1.3				PASS

2. Line code                  			4.1.4.2				PASS

3. Pulse shape (1)					4.6.2				PASS

4. Pulse shape (2)					4.1.1				PASS

5. Idle channel code					4.5.1				PASS

2.Layer 2 Conformance Test System Summary Report

Test Suite: CHT-96-PA-L2                Verdicts Assigned

PASS:74

FAIL: 0

INCONC:0

Selected Cases:   74

Test Identifier                            ITU-T REC. Q.921    Verdict

Test Group: DS70_V  State 7.0 Valid Frms

DS70_V01  Window Rotation                      5.9.5     PASS

Test Group: DL40_V  State 4.0 Valid Frms

DL40_V04  SABME/P=1                            5.5.1.2   PASS

DL40_V06  SABME/P=0                            5.5.1.2   PASS

DL40_V08  DISC/P=1                             5.5.4     PASS

DL40_V09  DISC/P=0                             5.5.4     PASS

DL40_V10  DM/F=1                               5.5.4     PASS

DL40_V11  DM/F=0                               5.5.4     PASS

Test Group: DL70_V  State 7.0 Valid Frms

DL70_V03  I Frame in Queue : Window Open       5.6.1     PASS

Dl70_V08  SABME/P=1                            5.5.2     PASS

DL70_V10  SABME/P=0                            5.5.2     PASS

DL70_V12  DISC/P=1                             5.5.3.2   PASS

DL70_V13  DISC/P=0                             5.5.3.2   PASS

DL70_V14  DM/F=0                               5.7.1     PASS

DL70_V16  DM/F=1                               5.8.7     PASS

DL70_V17  FRMR : Reject RR                     5.7.1     PASS

DL70_V20  RR/P=1 : N(R)=V(S)                   5.6.5     PASS

DL70_V21  RR/P=0 : N(R)=V(S)                   5.6.5     PASS

DL70_V23  RR/F=0 : N(R)=V(S)                   5.6.5     PASS

DL70_V27  RR/P=1 : V(A)=N(R)<V(S)              5.6.5     PASS

DL70_V28  RR/P=0 : V(A)=N(R)<V(S)              5.6.5     PASS

DL70_V29  RR/F=0 : V(A)=N(R)<V(S)              5.6.5     PASS

DL70_V30  REJ/P=1 : N(R)=V(S)                  5.6.4     PASS

DL70_V31  REJ/P=0 : N(R)=V(S)                  5.6.4     PASS

DL70_V32  REJ/F=0 : N(R)=V(S)                  5.8.7     PASS

DL70_V33  REJ/P=1 : V(A)<=N(R)<V(S)            5.6.4     PASS

DL70_V34  REJ/P=0 : V(A)<=N(R)<V(S)            5.6.4     PASS

DL70_V35  REJ/F=0 : V(A)<=N(R)<V(S)            5.8.7     PASS

DL70_V36  RNR/P=1 : N(R)=V(S)                  5.6.5     PASS

DL70_V37  RNR/P=0 : N(R)=V(S)                  5.6.5     PASS

DL70_V39  RNR/F=0 : N(R)=V(S)                  5.6.5     PASS

DL70_V40  RNR/P=1 : V(A)<=N(R)<V(S)            5.6.5     PASS

DL70_V41  RNR/P=0 : V(A)<=N(R)<V(S)            5.6.5     PASS

DL70_V43  RNR/F=0 : V(A)<=N(R)<V(S)            5.6.5     PASS

DL70_V44  I/P=1 : N(S)=V(R), N(R)=V(S)         5.6.2.1   PASS

DL70_V45  I/P=0 : N(S)=V(R), N(R)=V(S)         5.6.2.2   PASS

DL70_V46  I/P=1 : N(S)<>V(R), N(R)=V(S)        5.8.1     PASS

DL70_V47  I/P=0 : N(S)<>V(R), N(R)=V(S)        5.8.1     PASS

DL70_V52  I/P=1 : N(S)=V(R), V(A)=N(R)<V(S)    5.6.2.1   PASS

DL70_V53  I/P=0 : N(S)=V(R), V(A)=N(R)<V(S)    5.6.2.2   PASS

DL70_V54  I/P=1 : N(S)<>V(R), V(A)=N(R)<V(S)   5.8.1     PASS

DL70_V55  I/P=0 : N(S)<>V(R), V(A)=N(R)<V(S)   5.8.1     PASS

DL70_V56  T200 Timeout, RC<N200                5.6.7     PASS

DL70_V57  T203 Timeout                         5.10.3.3  PASS

Test Group: DL80_V  State 8.0 Valid Frms

DL80_V03  I Frame in Queue : Window Open       5.6.1     PASS

DL80_V08  SABME/P=1                            5.5.2     PASS

DL80_V10  SABME/P=0                            5.5.2     PASS

DL80_V12  DISC/P=1                             5.5.3.2   PASS

DL80_V13  DISC/P=0                             5.5.3.2   PASS

DL80_V14  DM/F=1                               5.7.1     PASS

DL80_V15  DM/F=0                               5.7.1     PASS

DL80_V17  FRMR : Reject RR                     5.7.1     PASS

DL80_V20  RR/P=1 : V(A)<=N(R)<=V(S)            5.6.5     PASS

DL80_V21  RR/P=0 : V(A)<=N(R)<=V(S)            5.6.5     PASS

DL80_V22  RR/F=1 : V(A)<=N(R)<=V(S)            5.6.5     PASS

DL80_V23  RR/F=0 : V(A)<=N(R)<=V(S)            5.6.5     PASS

DL80_V24  REJ/P=1 : V(A)<=N(R)<=V(S)           5.6.4     PASS

DL80_V25  REJ/P=0 : V(A)<=N(R)<=V(S)           5.6.4     PASS

DL80_V26  REJ/F=1 : V(A)<=N(R)<=V(S)           5.6.4     PASS

DL80_V27  REJ/F=0 : V(A)<=N(R)<=V(S)           5.6.4     PASS

DL80_V28  RNR/P=1 : V(A)<=N(R)<=V(S)           5.6.5     PASS

DL80_V29  RNR/P=0 : V(A)<=N(R)<=V(S)           5.6.5     PASS

DL80_V30  RNR/F=1 : V(A)<=N(R)<=V(S)           5.6.5     PASS

DL80_V31  RNR/F=0 : V(A)<=N(R)<=V(S)           5.6.5     PASS

DL80_V32  I/P=1 : N(S)=V(R), N(R)=V(S)         5.6.2.1   PASS

DL80_V33  I/P=0 : N(S)=V(R), N(R)=V(S)         5.6.2.2   PASS

DL80_V34  I/P=1 : N(S)<>V(R), N(R)=V(S)        5.8.1     PASS

DL80_V35  I/P=0 : N(S)<>V(R), N(R)=V(S)        5.8.1     PASS

DL80_V40  I/P=1 : N(S)=V(R), V(A)=N(R)<V(S)    5.6.2.1   PASS

DL80_V41  I/P=0 : N(S)=V(R), V(A)=N(R)<V(S)    5.6.2.2   PASS

DL80_V42  I/P=1 : N(S)<>V(R), V(A)=N(R)<V(S)   5.8.1     PASS

DL80_V43  I/P=0 : N(S)<>V(R), V(A)=N(R)<V(S)   5.8.1     PASS

DL80_V44  T200 Timeout, RC=N200                5.6.7     PASS

DL80_V45  T200 Timeout, RC<N200, V(A)<V(S)     5.6.7     PASS

DL80_V46  T200 Timeout, RC<N200, V(A)=V(S)     5.6.7     PASS

3.Layer 3 Conformance Test

Test Suite: CHT-96-PA-L3                Verdicts Assigned

PASS:      55

FAIL:       0

INCONC:     0

Selected Cases:  55

Test Identifier                          ITU-T REC. Q.931  Verdict

Test Group: Basic Interconnection Tests

1. Incoming Call (#21003)                      5.3.3     PASS

2. Outgoing Call (#11105)                      5.3.4     PASS

Test Group: U0  TESTS

#10001:  [RC2(1,16), NO_MSG]                   5.8.3     PASS

#10002:  [RL3(1,16), RC_81]                    5.8.3.2B) PASS

#10005:  [SU3(BC,CD#,LLC,HLC), AL+CN+CP]       5.2.4     PASS

#10006:  [SU2(SCI,BC,CD#,LLC,HLC), AL+CN+CP]   5.2.5     PASS

#10007:  [SU6(BC,LLC,HLC), AL+CN+CP]           5.2.6     PASS

#10008:  [SU4(IBCAP,LLC,HLC), RC_88+NO_MSG]    5.2.2     PASS

#20002:  [<IUT!SETUP>, SU]                     5.1.3     PASS

Test Group: U1  TESTS

#10101:  [CP2, NO_MSG, U3]                     5.1.5.1   PASS

#10102:  [RC2(1,16), NO_MSG, U0]               5.8.4     PASS

#10103:  [RL3(1,16), RC]                       5.3.2     PASS

#10106:  [SQ2, ST]                             5.8.10    PASS

Test Group: U3  TESTS

#10301:  [AL2, NO_MSG, U4]                     5.1.7     PASS

#10302:  [CN2, ST(97,8,101)+SQ+CA+NO_MSG]      5.1.8     PASS

#10303:  [DI2(1,16), RL]                       5.3.4     PASS

#10304:  [IN2(1), NO_MSG]                      5.2.4     PASS

#10305:  [PG2, NO_MSG]                         5.1.6     PASS

#10306:  [RC2(1,16), NO_MSG, U0]               5.8.4     PASS

#10307:  [RL3(1,16), RC]                       5.3.4     PASS

#10308:  [SQ2, ST]                             5.8.10    PASS

#20301:  [<IUT!DISC>, DI_16]                   5.3.3     PASS

Test Group: U4  TESTS

#10401:  [CN2, CA+NO_MSG]                      5.1.8     PASS

#10402:  [DI2(1,16), RL]                       5.3.4     PASS

#10403:  [IN2(1), NO_MSG]                      5.2.4     PASS

#10404:  [PG2, NO_MSG|ST]                      5.1.6     PASS

#10405:  [RC2(1,16), NO_MSG, U0]               5.8.4     PASS

#10406:  [RL3(1,16), RC]                       5.8.4     PASS

#10407:  [SQ2, ST]                             5.8.10    PASS

#20401:  [<IUT!DISC>, DI_16]                   5.3.3     PASS

Test Group: U8  TESTS

#10801:  [CA2, NO_MSG, U10]                    5.2.7     PASS

#10802:  [DI2(0,16), RL]                       5.3.4     PASS

#10803:  [IN2(0), NO_MSG]                      5.2.4     PASS

#10804:  [RC2(0,16), NO_MSG, U0]               5.8.4     PASS

#10805:  [RL3(0,16), RC]                       5.3.2     PASS

#10806:  [SQ2, ST]                             5.8.10    PASS

#20801:  [T313(4S) TIMEOUT, DI]                5.2.8     PASS

Test Group: U10 TESTS

#11001:  [DI2(0,16), RL]                       5.3.4     PASS

#11002:  [IN2(0), NO_MSG]                      5.2.4     PASS

#11003:  [NO2(0), NO_MSG]                      5.9       PASS

#11004:  [RC2(0,16), NO_MSG, U0]               5.8.4     PASS

#11005:  [RL3(0,16), RC]                       5.8.4     PASS

#11006:  [SQ2, ST]                             5.8.10    PASS

#21003:  [<IUT!DISC>, DI_16]                   5.3.3     PASS

Test Group: U11 TESTS

#11101:  [DI2(1,16), RL]                       5.3.5     PASS

#11102:  [IN2(1), NO_MSG]                      5.2.4     PASS

#11103:  [NO2(1), NO_MSG|ST]                   5.9       PASS

#11104:  [RC2(1,16), NO_MSG, U0]               5.8.4     PASS

#11105:  [RL3(1,16), RC]                       5.3.4     PASS

#21101: *[T305(30S) TIMEOUT, RL]               5.3.3     PASS

Test Group: U19 TESTS

#11902:  [IN2(0), NO_MSG|ST]                   5         PASS

#11903:  [RC2(0,16), NO_MSG, U0]               5.3.4     PASS

#11904:  [RL3(0,16), NO_MSG, U0]               5.3.5     PASS

#11905:  [SQ2, ST]                             5.8.10    PASS

#21901: *[T308(4S) TIMEOUT, RL]                5.3.3     PASS

# Text boxes

附件四

本書未經本局同意不得轉載翻印