Table 1: Stationary Pollution Source Air Pollutant Emissions Standards

| Air Pollutant | Emissions Standard | Conversion Constant | Date of Enforcement | Notes |
| --- | --- | --- | --- | --- |
|  | Emissions Pipe | Peripheral Boundary | a1 | a2 | New Pollution Sources | Existing Pollution Sources |  |
| Particulate Pollutant (Opacity) | Continuous automatic monitoring: 6 minute monitoring values for daily opacity may not exceed 20% of the accumulated time by over 4 hours. | － | － | － | Date of promulgation | Date of promulgation | The following equipment are not subject to restrictions: 1. Built-in engines smaller than 2500 cc 2. Equipment for laboratory use 3. Portable welding and soldering equipment 4. Pile drivers 5. Training equipment for visual determination of smoke 6. Equipment for fire drills or accidental fires |
|  | Visual determination of smoke: Opacity may not exceed 20%; when ending or starting operations, opacity can reach 40%; however, within one hour, the accumulated time for 20% opacity may not exceed 3 minutes. | － | － | － | Date of promulgation | Date of promulgation |  |
| Particulate Pollutant (Weight and Concentration) | (1) | 500 μg/Nm3 | 0.58 | 2.8×10-4 | － | Standard (1) shall take effect on the date of promulgation. | 1.Those that have not been listed in Standard (1) shall use the following calculation formula: C﹦1860.3Q-0.386 2.Particulate emission standard applies to objects, pollution sources established after April 25, 2013, shall be considered new pollution sources. Pollution sources established, under construction, has already completed construction project bidding or completed contract signing without bidding, shall be considered existing pollution sources. But exiting pollution source comply with the modified condition of Article 20 of Air Pollution Control Act shall be considered new pollution source. 3.Standard(2)、(3)、(4) shall use non-diluted dry exhaust volume as the calculation standard excepting the combustion process using heating furnace, cracking furnace and boiler. |
|  | Emissions Displacement Q (Nm3/min) | Concentration C (mg/Nm3) |  |  |  |  |  |  |
|  | 30 or less 50 100 200 300 500 800 1000 2000 3000 5000 8000 10000 20000 30000 50000 70,000 and higher | 500 411 314 241 206 169 141 129 99 85 70 58 53 41 35 29 25 |  |  |  |  |  |  |
|  | Combustion Process | (2)50 mg/Nm3 (3)100 mg/Nm3 |  |  |  | Standard (2) shall take effect on the date of promulgation. | Standard (3) shall take effect on the 2014.4.30 |  |
|  | External Combustion Process | (4)100 mg/Nm3 |  |  |  | Standard (4) shall take effect on the date of promulgation. | Standard (4) shall take effect on the 2014.4.30 |  |
| Sulfur Oxides (SOx expressed as SO2 ) | Combustion Process | Gas Fuel | 100 ppm | 0.3 ppm | 1.0 | 4.9×10-4 | Date of promulgation | Date of promulgation | Unless other regulations apply, emissions pipe standards for sulfur factories in the petroleum refining industry shall use 500 ppm as standard values. |
|  |  | Liquid Fuel | 300 ppm |  |  |  | Date of promulgation | Date of promulgation |  |
|  |  | Solid Fuel | 300 ppm |  |  |  | Date of promulgation | Date of promulgation |  |
|  | External Combustion Process | 650 ppm |  |  |  | Date of promulgation | Date of promulgation |  |
| Sulfuric Acid (SO3 or H2SO4 expressed as 100% H2SO4 ) | Sulfuric Acid Factories | 100 mg/Nm3 | 50 μg/Nm3 | 0.05 | 3.0×10-5 | Date of promulgation | Date of promulgation |  |
|  | Pollution Sources Other than Sulfuric Acid Factories | 200 mg/Nm3 |  |  |  |  |  |  |
| Nitrogen Oxides (NOx expressed as NO2 ) | Combustion Equipment | Gas Fuel | (1) 300 ppm | － | － | － | Standard (2) shall take effect nationwide on the date of promulgation. | Standard (2) takes effect of the date of promulgation in Taipei City, Kaohsiung City, New Taipei City, Pingtung County, Taitung County, and Hualien County. Other areas shall be subject to Standard (1). | 1. Boilers over 4 tons and other combustion equipment with thermal input of 2.64 x 10 6 kcal/hr or higher. 2. Mixed fuels shall use the following formulas to calculate emissions values: Emissions Limit = Ax+By+Cz Emissions using dry calculations A: Gas fuel of NOx emissions standards. B: Liquid fuel of NOx emissions standards. C: Solid fuel of NOx emissions standards. x: Gas fuel as a percentage of total thermal input volume. y: Liquid fuel as a percentage of total thermal input volume. z: Solid fuel as a percentage of total thermal input volume. |
|  |  |  | (2) 150 ppm |  |  |  |  |  |  |
|  |  | Liquid Fuel | (1) 400 ppm |  |  |  |  |  |  |
|  |  |  | (2) 250 ppm |  |  |  |  |  |  |
|  |  | Solid Fuel | (1) 500 ppm |  |  |  |  |  |  |
|  |  |  | (2) 350 ppm |  |  |  |  |  |  |
|  | Combustion Using Outside Manufacturing Processes | (1) 500 ppm | 0.25 ppm | 0.60 | 2.9×10-4 |  |  |  |
|  |  | (2) 250 ppm |  |  |  |  |  |  |
| Carbon Monoxide (CO) | 2000 ppm | － | － | － | Date of promulgation | Date of promulgation |  |
| Total Fluoride Content (measured as F- ) | 10 mg/Nm3 | 10 μg/Nm3 | 1.17×10-2 | 5.7×10-6 | Date of promulgation | Date of promulgation |  |
| Hydrogen Chloride (HC1) | 80 ppm or 1.8kg/hr or less. | 0.1 ppm | 0.19 | 9.0×10-5 | Date of promulgation | Date of promulgation |  |
| Chlorine Gas (Cl2) | 30 ppm | 0.02 ppm | 0.07 | 4.0×10-5 | Date of promulgation | Date of promulgation |  |
| Ammonia Gas (NH3) | Measured in accordance with methods listed in Article 7 | 1 ppm | 0.885 | 4.3×10-4 | Date of promulgation | Date of promulgation |  |
| Hydrogen Sulfide (H2S) | Atmospheric output of 100 ppm | 0.1 ppm | 0.177 | 9.0×10-5 | Date of promulgation | Date of promulgation |  |
|  | Before combustion processing, an entrance concentration of 650 ppm |  |  |  |  |  |  |
| Mercaptan (RSH measured as CH3SH) | Measured in accordance with methods listed in Article 7 | 0.01 ppm | 0.025 | 1.2×10-5 | Date of promulgation | Date of promulgation |  |
| Methyl Sulfide (CH3)2S) | Measured in accordance with methods listed in Article 7 | 0.2 ppm | 0.646 | 3.1×10-4 | Date of promulgation | Date of promulgation |  |
| Methyl Disulfide ((CH3)2S2) | Measured in accordance with methods listed in Article 7 | 0.1 ppm | 0.49 | 2.4×10-4 | Date of promulgation | Date of promulgation |  |
| Monomethylamine (CH3NH2) | Measured in accordance with methods listed in Article 7 | 0.02 ppm | 0.032 | 1.6×10-5 | Date of promulgation | Date of promulgation |  |
| Dimethylamine ((CH3)2NH) | Measured in accordance with methods listed in Article 7 | 0.02 ppm | 0.047 | 2.3×10-5 | Date of promulgation | Date of promulgation |  |
| Trimethylamine ((CH3)3N) | Measured in accordance with methods listed in Article 7 | 0.02 ppm | 0.061 | 3.0×10-5 | Date of promulgation | Date of promulgation |  |
| Carbon Disulfide (CS2) | Measured in accordance with methods listed in Article 7 | 0.4 ppm | 1.58 | 7.7×10-4 | Date of promulgation | Date of promulgation |  |
| Formaldehyde (HCHO) | Measured in accordance with methods listed in Article 7 | 0.2 ppm | 0.31 | 1.5×10-4 | Date of promulgation | Date of promulgation |  |
| Benzene (C6H6) | Measured in accordance with methods listed in Article 7 | 0.5 ppm | 2.03 | 9.9×10-4 | Date of promulgation | Date of promulgation | C1, C2, C3 are the actual measured concentrations of benzene, toluene, and xylenes, respectively. S1, S2, S3 are the concentrations of benzene, toluene, and xylenes, respectively, at the peripheral boundary. |
| Toluene (C6H5CH3) | Measured in accordance with methods listed in Article 7 | 2 ppm | 9.58 | 4.66×10-3 | Date of promulgation | Date of promulgation |  |
| Xylenes (C6H4 (CH3)2) | Measured in accordance with methods listed in Article 7 | 2 ppm | 10.0 | 5.36×10-3 | Date of promulgation | Date of promulgation |  |
| Plumbum (Pb) | 10 mg/Nm3 | 10 μg/Nm3 | 1.17×10-2 | 5.7×10-6 | Date of promulgation | Date of promulgation |  |
| Cadmium (Cd) | 1 mg/Nm3 | 0.5 μg/Nm3 | 5.8×10-4 | 2.8×10-7 | Date of promulgation | Date of promulgation |  |
| Asbestos and Substances Containing Asbestos | Invisible to the naked eye | Invisible to the naked eye | － | － | Date of promulgation | Date of promulgation |  |
| Vinyl Chloride Monomer | 10 ppm | 0.2 ppm | 0.65 | 3.2×10-4 | Date of promulgation | Date of promulgation |  |
| Other Air Pollutants (See Table 2) | Measured in accordance with methods listed in Article 7 | A/50 | 8.5×10-3×A | 1.1×10-5×A | Date of promulgation | Date of promulgation | A: Table 2 lists the standards for allowable concentration of hazardous substances in the air in labor operations environments, in units of mg/m3). |
| Malodorous pollutants | Height h (meters) | Standard value | Areas | Standard value | － | － | Emissions pipe and peripheral boundary emissions standards (2) and (3) shall take effect on the date of promulgation. . | 1. Emissions pipe emissions standards shall take effect one year after the date of promulgation. 2. Peripheral boundary standards (1) and (3) shall take effect on the date of promulgation. | The concentrations of malodorous pollutants are dimensionless mathematical operator values, so there are no units of measure. 2. Definition of an industrial park: Land for industrial use of an area, part of an industrial zone or urban planning industrial park. 3. Definition of an agricultural district: 1. Urban planning agricultural districts, or zone delineations according to law, which have been determined by the urban planning competent authority to be part of an agricultural business zone. 2. According to the Regional Planning Act, special agricultural districts, common agricultural districts, forest areas and other areas in which land is designated for farming and grazing, aquiculture, forestry, and land for use for other special industrial purposes including agriculture and livestock, and wastewater treatment facilities. 3. Other land as determined by the central competent authority in consultation with the central agricultural industry competent authority. 4. Peripheral boundary emissions standard (2) is applicable to new pollution sources located in industrial parks or agricultural districts. However, pollution sources located in existing livestock farms in agricultural districts that have been upgraded but that are operating on an unchanged scale shall be subject to emissions standards for existing pollution sources. 5. Standards applied to all sampling locations shall serve as supporting data. 6. New pollution sources subject to malodorous pollutant emissions standards shall refer to pollution sources established after September 13, 2007 (inclusive); existing pollution sources refer to pollution sources established before September 13, 2007. |
|  | h≤18 18<h≤50 h>50 | 1000 2000 4000 When air quality model estimates for emissions pipes over 100 meters in height comply with the emissions pipe concentration values corresponding to the peripheral boundary standards for the area influenced by that pollution source, those concentrations may be taken as the standard values after reporting to and obtaining the central competent authority's approval. | Industrial Parks and Agricultural | (1) 50 (2) 30 |  |  |  |  |  |
|  |  |  | Areas Other than Industrial Parks and Agricultural Districts | (3) 10 |  |  |  |  |  |