Article 3	Terms and Symbols used in these Standards are defined as follows:

- “Peripheral boundary” means the boundary line marking the use or management of public or private premises.

- “mg” means milligram, equivalent to 0.001 grams.

- “μg” means microgram, equivalent to 0.001 milligrams.

- “K” means Kelvin absolute temperature scale, where K=273+°C.

- “Nm3” means 273 degrees Kelvin (273 K) and a volume of one atmosphere per cubic meter.

- “ppm” means parts per million.

- “q” means the “highest permissible emissions quantity per unit time” of each pollutant from each emissions pipe unit in a single pollution source, measured in grams per second (g/s).

- “a1” and “a2” mean the conversion constants for each pollutant.

- “k” means the diffusion coefficient for pollutant emissions, measured in grams per second per square meter (g/s•m2).

- “h” means the actual height of the outlet of the emissions pipe, measured in meters (m).

- “△h” means the height of smoke plume from the outlet of the emissions pipe, measured in meters (m).

- “he” means the effective height of outlet of emissions pipe he=h+△h, measured in meters (m).

- “Qh” means the heat emissions rate from a emissions pipe exhaust, measured in calories per second (cal/s).

- “Vs:” means emissions pipe outlet exhaust speed, measured in meters per second (m/s).

- “ds” means the internal diameter of the emissions pipe outlet, measured in meters per second (m).

- “ρ” means exhaust density, measured in grams per liter (g/l).

- “Cp” means specific heat at constant pressure from exhaust, measured in calories per gram degree Kelvin (cal/g•K).

- “Ts” means exhaust temperature at the exhaust pipe outlet, measured in Kelvin (K).

- “T” means ambient temperature surrounding the emissions pipe outlet, measured in degrees Kelvin (K).

- “” means annual average wind speed at the height of the emissions pipe outlet, measured in meters per second (m/s)  =  (h/10)0.2

- “” means average wind speeds at 10 meters high from the ground surface, measured in meters per second (m/s). These standards are based on an average wind speed of 3.5 meters per second (m/s) as the calculation reference standard.

- “Q” means displacement that has either undergone calibration or does not need calibration, measured in cubic meters per minute (Nm3/min).

- “Qs” means the measured displacement derived from testing methods, measured in cubic meters per minute (Nm3/min).

- “C” means concentration of pollutant emissions that has either undergone calibration or does not need calibration, measured in ppm or mg /Nm3.

- “Cs” means pollution emissions concentration based on testing methods, measured in ppm or mg /Nm3.

- “On” means standard percentage value of oxygen that is contained in exhaust, measured in %.

- “Os” means the actual testing value percentages of oxygen content in exhaust. If value exceeds 20%, then value shall be calculated as 20%.