Article 7	Gas pollutants that fail to be listed in standards for emissions pipes shall be calculated in accordance with the following methods for standards for emissions pipes:

- When a low emissions pipe is h(6m (meters).

q = a2·b2

b: the minimum horizontal distance from the emissions pipe outlet of the pollution source to the peripheral boundary of the pollution source, in units of m (meters).

- When a taller emissions pipe is h > 6m

b': the minimum distance from the emissions pipe outlet of the pollution source to the peripheral boundary line of the pollution source at a vertical height of 6m (meters), in units of m (meters).

b": The minimum distance from the center of the emission pipe outlet to the building when the conical area of a pollution source measured at a downward 12 degree angle from the center of an emissions pipe outlet intersects with the buildings of other people (with the exception of unoccupied storage warehouse buildings), in units of m (meters).

C.	When b < 5 (h-6) and does not fall under the conditions of subparagraph 2, which means that when the distance from the pollution source to a building is very far or a building is lower than 6 m (meters), the conical area of a pollution source measured at a downward 12 degree angle from the center of an emissions pipe outlet does not intersect with the buildings of other people.

# Text boxes

Illustration of claculation

Peripheral Boundary

Building